Manual sealless steel strapping tool with MicroLock™

Characteristics

| Strapping qualities: | Uniflex and Ultraflex max. 1100 N/mm2 / 160’000 psi |
| --- | --- |
| Strapping dimensions: widths thicknesses | 9.5 – 20.0 mm / 3/8 – ¾” 0.38 – 0.63 mm / .015 – .025” |
| Weights: | 4.45 kg / 9.8 lbs Normal-version 4.7 kg / 10.4 lbs TW-version |
| Sealless joint: | Fromm MicroLock™ |
| Average seal strength: | approx. 80 % |
| TW-version available: | Torque wrench tensioning system |
| Suspension (Optional): | Suspension for vertical and horizontal applications; has to be ordered separately Handle for horizontal applications; has to be ordered separately |

Advantages

- The MicroLock™ sealles system guarantees a maximum of security of the sealless steel strapping joint against unlocking

- The tool can handle regular duty and high tensile steel strapping

- The tool can handle steel strapping up to a thickness of 0.64 mm / .025”

- Thanks to the special tensioning system (free wheeling) no loss of strap tension

- The sealing mechanism is completely closed

- The adjustment of the cutting and sealing depth is simple

- The feed wheel and the die and cutter support are easy to change

Chart of types model A337

| Item No. | Model | Uniflex and Ultraflex max. 1100 N/mm2 / 160'000 psi Width Thicknesses |
| --- | --- | --- |
|  |  | mm | inch | mm | inch |
| 13.1850 | A337/9.5/0.38-0.50 | 9.5 | 3/8“ | 0.38-0.50 | .015-.020 |
| 13.1860 | A337/10/0.38-0.50 | 10 |  | 0.38-0.50 | .015-.020 |
| 13.1870 | A337/12.7/0.38-0.50 | 12.7 | 1/2” | 0.38-0.50 | .015-.020 |
| 13.1872 | A337/12.7/0.50-0.63 | 12.7 | 1/2” | 0.50-0.63 | .020-.025 |
| 13.1880 | A337/13/0.38-0.50 | 13 |  | 0.38-0.50 | .015-.020 |
| 13.1882 | A337/13/0.50-0.63 | 13 |  | 0.50-0.63 | .020-.025 |
| 13.1890 | A337/16/0.38-0.50 | 16 | 5/8” | 0.38-0.50 | .015-.020 |
| 13.1892 | A337/16/0.50-0.63 | 16 | 5/8” | 0.50-0.63 | .020-.025 |
| 13.1910 | A337/19/0.38-0.50 | 19 | 3/4” | 0.38-0.50 | .015-.020 |
| 13.1912 | A337/19/0.50-0.63 | 19 | 3/4” | 0.50-0.63 | .020-.025 |
| 13.1920 | A337/20/0.38-0.50 | 20 |  | 0.38-0.50 | .015-.020 |
| 13.1922 | A337/20/0.50-0.63 | 20 |  | 0.50-0.63 | .020-.025 |

Chart of types model A337 with torque wrench tensioning system

| Item No. | Model | Uniflex and Ultraflex max. 1100 N/mm2 / 160'000 psi Width Thicknesses |
| --- | --- | --- |
|  |  | mm | inch | mm | inch |
| 13.1851 | A337/9.5/0.38-0.50/TW | 9.5 | 3/8“ | 0.38-0.50 | .015-.020 |
| 13.1861 | A337/10/0.38-0.50/TW | 10 |  | 0.38-0.50 | .015-.020 |
| 13.1871 | A337/12.7/0.38-0.50/TW | 12.7 | 1/2” | 0.38-0.50 | .015-.020 |
| 13.1873 | A337/12.7/0.50-0.63/TW | 12.7 | 1/2” | 0.50-0.63 | .020-.025 |
| 13.1881 | A337/13/0.38-0.50/TW | 13 |  | 0.38-0.50 | .015-.020 |
| 13.1883 | A337/13/0.50-0.63/TW | 13 |  | 0.50-0.63 | .020-.025 |
| 13.1891 | A337/16/0.38-0.50/TW | 16 | 5/8” | 0.38-0.50 | .015-.020 |
| 13.1893 | A337/16/0.50-0.63/TW | 16 | 5/8” | 0.50-0.63 | .020-.025 |
| 13.1911 | A337/19/0.38-0.50/TW | 19 | 3/4” | 0.38-0.50 | .015-.020 |
| 13.1913 | A337/19/0.50-0.63/TW | 19 | 3/4” | 0.50-0.63 | .020-.025 |
| 13.1921 | A337/20/0.38-0.50/TW | 20 |  | 0.38-0.50 | .015-.020 |
| 13.1923 | A337/20/0.50-0.63/TW | 20 |  | 0.50-0.63 | .020-.025 |

TW = Torque wrench tensioning system

Accessories

| A33.0121 | Suspension for vertical and horizontal applications |
| --- | --- |
| A33.0122 | Handle for horizontal applications |