Manual sealless steel strapping tool for high tension

Characteristics

| Strapping qualities: | Uniflex and Ultraflex max. 1100 N/mm2 / 160’000 psi |
| --- | --- |
| Strapping dimensions: widths thicknesses | 12.7 – 19.0 mm / ½ – ¾” 0.50 – 0.70 mm / .020 – .028” |
| Weights: | 5.7 kg / 12.6 lbs Normal-version 5.9 kg / 13.0 lbs TW-version |
| Average seal strength: | approx. 80 % |
| TW-version available: | Torque wrench tensioning system |
| Suspension (Optional): | Suspension for vertical and horizontal applications; has to be ordered separately Handle for horizontal applications; has to be ordered separately |

Advantages

- The special tensioning gear-system allows a high strap tension of up to 5500 N (1240 lbs) with a limited amount of tensioning effort of only 240 N (54 lbs)

- Handy sealless combination tool to strap flat packages (e.g. pallets, bales, crates, cases, various packages)

- Permits a very easy and efficient operation and outperforms other strapping tools by its ruggedness and its high reliability

- The sealless joint reduces the overall strapping costs by approx. 10% through the elimination of the seals

Chart of types model A338

| Item No. | Model | Width | Uniflex Thicknesses | Ultraflex Thicknesses |
| --- | --- | --- | --- | --- |
|  |  | mm | inch | mm | inch | mm | Inch |
| 13.2910 | A338/12.7/0.50-0.64 | 12.7 | 1/2“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2915 | A338/12.7/0.70/UNI | 12.7 | 1/2“ | 0.70 | .028 | - | - |
| 13.2920 | A338/13/0.50-0.64 | 13 |  | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2925 | A338/13/0.70/UNI | 13 |  | 0.70 | .028 | - | - |
| 13.2930 | A338/16/0.50-0.64 | 16 | 5/8“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2935 | A338/16/0.70/UNI | 16 | 5/8“ | 0.70 | .028 | - | - |
| 13.2940 | A338/19/0.50-0.64 | 19 | 3/4“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2945 | A338/19/0.70/UNI | 19 | 3/4“ | 0.70 | .028 | - | - |

Uniflex	= Regular duty strapping max. 850 N/mm2 / 123'000 psi
Ultraflex	= High tensile strapping max. 1100 N/mm2 / 160'000 psi

Chart of types model A338 with torque wrench tensioning system

| Item No. | Model | Width | Uniflex Thicknesses | Ultraflex Thicknesses |
| --- | --- | --- | --- | --- |
|  |  | mm | inch | mm | inch | mm | Inch |
| 13.2911 | A338/12.7/0.50-0.64/TW | 12.7 | 1/2“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2916 | A338/12.7/0.70/UNI/TW | 12.7 | 1/2“ | 0.70 | .028 | - | - |
| 13.2921 | A338/13/0.50-0.64/TW | 13 |  | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2926 | A338/13/0.70/UNI/TW | 13 |  | 0.70 | .028 | - | - |
| 13.2931 | A338/16/0.50-0.64/TW | 16 | 5/8“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2936 | A338/16/0.70/UNI/TW | 16 | 5/8“ | 0.70 | .028 | - | - |
| 13.2941 | A338/19/0.50-0.64/TW | 19 | 3/4“ | 0.50-0.64 | .020-.025 | 0.50-0.64 | .020-.025 |
| 13.2946 | A338/19/0.70/UNI/TW | 19 | 3/4“ | 0.70 | .028 | - | - |

Uniflex	= Regular duty strapping max. 850 N/mm2 / 123'000 psi
Ultraflex	= High tensile strapping max. 1100 N/mm2 / 160'000 psi

TW = Torque wrench tensioning system

Accessories

| A33.5301 | Suspension for vertical and horizontal applications |
| --- | --- |
| A33.5307 | Handle for horizontal applications |