Manual pusher type combination steel strapping tool

Characteristics

| Strapping qualities: | Uniflex and Ultraflex max. 1100 N/mm2 / 160’000 psi |
| --- | --- |
| Strapping dimensions: widths thicknesses | 10.0 – 19.0 mm / 3/8 – 3/4” 0.38 – 0.63 mm / .015 – .025” |
| Weight: | 3.4 kg / 7.5 lbs |
| Average seal strength: | approx. 75 % |
| Seals: | Overlap seals, see chart |
| Type of joint: | Single notch joint |

Advantages

- Very suitable for strapping of bars, bundles, tubes coils and items
with a small surface

- Independent from any energy source since operated manually

Chart of types model A431

| Item No. | Model | Uniflex and Ultraflex max. 1100 N/mm2 / 160'000 psi Width Thicknesses |
| --- | --- | --- |
|  |  | mm | inch | mm | inch |
| 13.3050 | A431/10/0.38-0.63/UNI | 10 | 3/8“ | 0.38-0.63 | .015-.025 |
| 13.3070 | A431/13/0.38-0.63/UNI | 13 | 1/2“ | 0.38-0.63 | .015-.025 |
| 13.3090 | A431/16/0.38-0.63/UNI | 16 | 5/8“ | 0.38-0.63 | .015-.025 |
| 13.3110 | A431/19/0.38-0.63/UNI | 19 | 3/4“ | 0.38-0.63 | .015-.025 |
| 13.3051 | A431/10/0.38-0.63/ULT | 10 | 3/8“ | 0.38-0.63 | .015-.025 |
| 13.3071 | A431/13/0.38-0.63/ULT | 13 | 1/2“ | 0.38-0.63 | .015-.025 |
| 13.3091 | A431/16/0.38-0.63/ULT | 16 | 5/8“ | 0.38-0.63 | .015-.025 |
| 13.3111 | A431/19/0.38-0.63/ULT | 19 | 3/4“ | 0.38-0.63 | .015-.025 |

Uniflex (UNI)	= Regular duty strapping max. 850 N/mm2 / 123'000 psi
Ultraflex (ULT) 	= High tensile strapping max. 1100 N/mm2 / 160'000 psi

Recommended seals

| Width mm | Inch | Dimensions (W, L, T) mm inch |
| --- | --- | --- |
| 10 | 3/8“ | 10 x 22 x 0.6 | 3/8 x 7/8 x .024 |
| 13 | 1/2“ | 13 x 22 x 0.6 | ½ x 7/8 x .024 |
| 16 | 5/8“ | 16 x 22 x 0.6 | 5/8 x 7/8 x .024 |
| 19 | ¾“ | 19 x 22 x 0.6 | 3/4 x 7/8 x .024 |

Tensile strength of the seal material: 600 N/mm² / 87’000 psi